## Slide 1: Presentation on
PRE-FLC
FOR
EVMs (CU:7514 & BU:7409)
OF
SEC-MP

## Slide 2
Physical Inspection:
Remove address tags, Ballot Paper, old stickers if any.
Visually inspect BU / CU for physical defects like breakage of moulded housing and latches, buttons missing, BU acrylic sheet cracked, cable & connector damaged etc.
Check all switches and doors of CU / BU for satisfactory working.
Sample Check list given as Annexure- III (For CU) & IV (For BU)

## Slide 3
Checking of Date and Time:
Insert battery pack and DMM in CU and Switch on. Verify the Date and time with the normal time. In case of any deviation adjust date and time in the CU.
Date and Time can be set by using the following method.
Ensure CU must be in CLEAR STATE.
Connect BU to CU.
Press and hold Result2 key and power on CU.
Press and hold Total key while displaying Stars on CU display.
Observe following format blinks continuously
DTE DD MM YY
TME HH MM SS

## Slide 4
Checking of Date and Time:
Enter DATE TIME values by using BU keys. As keys are pressed on BU, the entered digits are displayed on CU display.
(BU key board acts like following way
BU keys 1 to 9 for digits 1 to 9.
BU key 10 for digit 0
BU key 15 for BACKSPACE
BU key 16 for ENTER(SAVE entered values)
BU keys 11,12,13 and 14 Reserved)
After entering the time press BU key 16 for end of the setting. Note the time. Switch off the CU and again switch ON after at least 1 minute. Observe updated time. If it is updated, then it is passed, else mention in fault report as Time up-dation Error.

## Slide 5
Verification of Sr. No of CU & DMM:
Compare the serial no displayed with the serial Nos marked on the CU and DMM.
If there is discrepancy reject the respective units.

## Slide 6
BU Self Check:
Connect Three BUs to CU using BU cables and position the respective slide switches as per the BU position.
Press and hold Result1 key and power on CU.
Observe Link Error4 on CU display.
Observe LEDs glowing in sequence automatically on BU1, BU2 & BU3 from 1 to 16 followed by LED glow as per slide switch position.
Now press each and every key five times in sequence from Candidate 1 to Candidate 16 on each BU and observe corresponding LED blinks for every key press. During this process the Green LED (Ready LED)will glow on the BUs.

## Slide 7
CU Self Check:
Press and Hold Result2 key and power on CU.
Observe RTC Battery Status RTC BATTERY HIGH/LOW / CLOCK ERROR.
Observe display patterns (Digits 0 to 9 and stars Displayed on All CU characters in sequence)
When CU becomes Blank press TOTAL key to enter key check mode (Observe “0” displayed on the CU display),
Press each key 10 times in the following sequence (Observe corresponding digit displayed on the screen on top row, 6th position while pressing each key).

## Slide 8
CU Self Check: Contd.....
Key name Displayed digit
CLOSE 1
RESULT2 2
RESULT1 3
BALLOT 4
CAND. SET 5
TOTAL 6
CLEAR 7

## Slide 9
Voting Verification
Candidate Set for Voting Verification:
No. of Posts 3
Post 1 (in BU 1)
No of Candidates 15
No of seats 01
Post 2 (in BU 2)
No of Candidates 15
No of seats 01
Post 3 (in BU 3)
No of Candidates 15
No of seats 01
Carry out voting on all the EVMs with the above candidate set configuration and perform voting of at-least one vote to each candidate. Also perform at-least one under votes and one unfinished Voters. Compare the results and clear the data on CU.

## Slide 10
Completing Pre FLC:
Affix stickers on passed CU/BU after successful checking. Put unit serial number on the sticker and sign with date. (Sample format Annexure-I)
Affix stickers on defective CU/BU after successful checking. Put unit serial number on the sticker and sign with date. (Sample format Annexure-II
Maintain the record of faulty CU (Annexure – III) & BU (Annexure-IV) mentioning specific reason.
Place the CU/BU in the appropriate carrying case.

## Slide 11
Clearing CU after changing DMM:
(procedure for handling Memory changed message issues)
Change the DMM when CU in power off mode.
Connect BU(slide switch position at 1) to CU
Power on CU.
Observe CU displays following messages
  SEC MP
  MEMORY CHANGED
Case 1: CU in RESULT state & CLEAR state
Press and hold CLEAR key on CU till the DELETING POLLED VOTES message displays on CU.
Case 2: CU in other than RESULT state& CLEAR state
Press and hold CLEAR key on CU and observe INVALID message.
Press and hold both CAND. SET key and CLEAR key simultaneously till the DELETING POLLED VOTES message displays on CU.
Note: Check for ‘’BEEP’’ sound followed by every display message.

## Slide 12
Annexure-I (Sample Sticker)
Pre FLC PASSED | 
Name of District | 
Name of Location | 
CU/BU Serial Number | 
Pre FLC done as per procedure | 
Signature of official who has done Pre FLC | 
Date of Pre FLC | 
Signature of Supervising official | 

## Slide 13
Annexure-II (Sample Sticker)
Pre FLC REJECTED | 
Name of District | 
Name of Location | 
CU/BU Serial Number | 
Type of Error/ Fault Description | 
Signature of official who has done Pre FLC | 
Date of Pre FLC | 
Signature of Supervising official | 

## Slide 14
Annexure-III (Faulty CU Report)
 |  |  |  |  |  |  |  | Annexure-III
STATE ELECTION COMMISSION - MADHYA PRADESH |  |  |  |  |  |  |  | 
Pre FLC ( DETAILS OF FAULTY CONTROL UNIT) |  |  |  |  |  |  |  | 
District : |  |  |  | Place of Testing : |  |  | Date: | 
 |  |  |  | 1 | 2 | 3 | 4 | TOTAL
Sl.No. of Unit => |  |  |  |  |  |  |  | COUNT
1 | Visual Inspection | Display section | On / Busy lamp cover missing |  |  |  |  | 
2 |  |  | Display panel cover broken/ missing |  |  |  |  | 
3 |  | Candidate set section | Candidate Set section cover broken/ missing |  |  |  |  | 
4 |  |  | Candidate Set inside door broken/ missing |  |  |  |  | 
5 |  |  | Plug for power pak broken |  |  |  |  | 
6 |  |  | Provision for thread seal / latch broken |  |  |  |  | 
7 |  |  | Cand set button missing |  |  |  |  | 
8 |  | Result Section | Result Set section inner compartment door broken/ not working |  |  |  |  | 
9 |  |  | Result Set section outer compartment door broken/ not working |  |  |  |  | 
10 |  |  | Provision for thread seal / latch broken |  |  |  |  | 
11 |  |  | Any button missing (Name of button) |  |  |  |  | 
12 |  | Ballot section | Any button missing (Name of button) |  |  |  |  | 
13 |  | Rear-side | Rear-side compartment Cover missing/ broken |  |  |  |  | 
14 |  |  | ON/OFF switch broken |  |  |  |  | 
15 |  |  | BU Connector broken |  |  |  |  | 
16 |  |  | DI Connector broken |  |  |  |  | 
17 | Operational Iinspection |  | Dead |  |  |  |  | 
18 |  |  | ON/OFF switch not working |  |  |  |  | 
18 |  |  | Busy lamp Not Glowing/ flickering |  |  |  |  | 
19 |  |  | ON lamp Not Glowing/ flickering |  |  |  |  | 
20 |  |  | Display segments problem |  |  |  |  | 
21 |  |  | Buzzer Not Working/ Continuous |  |  |  |  | 
22 |  |  | Serial No of CU Mismatch |  |  |  |  | 
23 |  |  | Link Error |  |  |  |  | 
24 |  |  | Pressed Error |  |  |  |  | 
25 |  |  | Error |  |  |  |  | 
26 |  |  | CU Error |  |  |  |  | 
27 |  |  | Clock Error |  |  |  |  | 
28 |  |  | Time updation Error |  |  |  |  | 
29 |  |  | Displays "Tampered" |  |  |  |  | 
30 |  |  | Displays "Security not Configured" |  |  |  |  | 
31 |  |  | Change Battery Error |  |  |  |  | 
32 |  |  | Buttons Not Working (Mention name of button) |  |  |  |  | 
33 |  |  | Others (desribe few lines) |  |  |  |  | 
 |  |  | Tested By : |  |  | Repaired By : |  | 
 |  |  | Signature : |  |  | Signature : |  | 
 |  |  | Name .: |  |  | Name .: |  | 
 |  |  | Code No .: |  |  | Code No .: |  | 
 |  |  |  |  |  | Date of Repair: |  | 

## Slide 15
Annexure-IV (Faulty BU Report)
STATE ELECTION COMMISSION - MADHYA PRADESH |  |  |  |  |  |  |  |  |  |  |  | 
Pre FLC ( DETAILS OF FAULTY BALLOT UNIT) |  |  |  |  |  |  |  |  |  |  |  | 
 |  | District : |  | Place of Testing : |  |  | Quantity : |  |  | Date : |  | 
 |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Sl.No. of Unit => |  |  |  |  |  |  |  |  |  |  |  | 
1 | Visual Inspection | Cabinet/ side lock broken |  |  |  |  |  |  |  |  |  | 
2 |  | Ballot Paper transparent screen broken |  |  |  |  |  |  |  |  |  | 
3 |  | Top cover side locks broken/ missing |  |  |  |  |  |  |  |  |  | 
4 |  | Candidates button masking tab broken/ missing (Nos) |  |  |  |  |  |  |  |  |  | 
5 |  | Candidates button broken/ missing (Nos) |  |  |  |  |  |  |  |  |  | 
6 |  | Connector hood broken |  |  |  |  |  |  |  |  |  | 
7 |  | Red latch of hood missing/ broken |  |  |  |  |  |  |  |  |  | 
8 |  | Black latch of hood missing/ broken |  |  |  |  |  |  |  |  |  | 
9 |  | Slide Switch broken |  |  |  |  |  |  |  |  |  | 
10 |  | Inerconnecting BU Cover broken |  |  |  |  |  |  |  |  |  | 
11 |  | Others (desribe few lines) |  |  |  |  |  |  |  |  |  | 
12 | Operational Inspection | Ready Lamp Not Glowing |  |  |  |  |  |  |  |  |  | 
13 |  | Ready Lamp glow continuous |  |  |  |  |  |  |  |  |  | 
14 |  | Candidates button LED glow continuous (No/s) |  |  |  |  |  |  |  |  |  | 
15 |  | Candidates button LED not glowing (No/s) |  |  |  |  |  |  |  |  |  | 
16 |  | Pressed Error |  |  |  |  |  |  |  |  |  | 
17 |  | Link Error |  |  |  |  |  |  |  |  |  | 
18 |  | 9 to 16 candidates lamps ON (BU Tampered) |  |  |  |  |  |  |  |  |  | 
19 |  | Slide Switch not working |  |  |  |  |  |  |  |  |  | 
20 |  | Buttons Not Working (Mention serial number of button from top) |  |  |  |  |  |  |  |  |  | 
21 |  | Connector/ cable problem |  |  |  |  |  |  |  |  |  | 
22 |  | Others (desribe few lines) |  |  |  |  |  |  |  |  |  | 
 |  |  | Tested By : |  |  |  | Repaired By : |  |  |  |  | 
 |  |  | Signature : |  |  |  | Signature : |  |  |  |  | 
 |  |  | Name .: |  |  |  | Name .: |  |  |  |  | 
 |  |  | Code No .: |  |  |  | Code No .: |  |  |  |  | 
 |  |  |  |  |  |  | Date of Repair: |  |  |  |  | 

## Slide 16
Annexure-V (Faulty CU Summary)
 |  |  |  | SUMMARY SHEET |  |  |  | Annexure-V
STATE ELECTION COMMISSION - MADHYA PRADESH |  |  |  |  |  |  |  | 
Pre FLC ( DETAILS OF FAULTY CONTROL UNIT) |  |  |  |  |  |  |  | 
District : |  |  |  | Place of Testing : |  |  | Date: | 
Name of District => |  |  |  | District-1 | District-2 | District-3 | District-4 | TOTAL
 |  |  |  | Count | Count | Count | Count | COUNT
1 | Visual Inspection | Display section | On / Busy lamp cover missing |  |  |  |  | 
2 |  |  | Display panel cover broken/ missing |  |  |  |  | 
3 |  | Candidate set section | Candidate Set section cover broken/ missing |  |  |  |  | 
4 |  |  | Candidate Set inside door broken/ missing |  |  |  |  | 
5 |  |  | Plug for power pak broken |  |  |  |  | 
6 |  |  | Provision for thread seal / latch broken |  |  |  |  | 
7 |  |  | No of buttons missing |  |  |  |  | 
8 |  | Result Section | Result Set section inner compartment door broken/ not working |  |  |  |  | 
9 |  |  | Result Set section outer compartment door broken/ not working |  |  |  |  | 
10 |  |  | Provision for thread seal / latch broken |  |  |  |  | 
11 |  |  | No of buttons missing |  |  |  |  | 
12 |  | Ballot section | No of buttons missing |  |  |  |  | 
13 |  | Rear-side | Rear-side compartment Cover missing/ broken |  |  |  |  | 
14 |  |  | ON/OFF switch broken |  |  |  |  | 
15 |  |  | BU Connector broken |  |  |  |  | 
16 |  |  | DI Connector broken |  |  |  |  | 
17 | Operational Iinspection |  | Dead |  |  |  |  | 
18 |  |  | ON/OFF switch not working |  |  |  |  | 
18 |  |  | Busy lamp Not Glowing/ flickering |  |  |  |  | 
19 |  |  | ON lamp Not Glowing/ flickering |  |  |  |  | 
20 |  |  | Display segments problem |  |  |  |  | 
21 |  |  | Buzzer Not Working/ Continuous |  |  |  |  | 
22 |  |  | Serial No of CU Mismatch |  |  |  |  | 
23 |  |  | Link Error |  |  |  |  | 
24 |  |  | Pressed Error |  |  |  |  | 
25 |  |  | Error |  |  |  |  | 
26 |  |  | CU Error |  |  |  |  | 
27 |  |  | Clock Error |  |  |  |  | 
28 |  |  | Time updation Error |  |  |  |  | 
29 |  |  | Displays "Tampered" |  |  |  |  | 
30 |  |  | Displays "Security not Configured" |  |  |  |  | 
31 |  |  | Change Battery Error |  |  |  |  | 
32 |  |  | No of Buttons Not Working |  |  |  |  | 
33 |  |  | Others (desribe few lines) |  |  |  |  | 
 |  |  | Tabulated By : |  |  |  |  | 
 |  |  | Signature : |  |  |  |  | 
 |  |  | Name .: |  |  |  |  | 
 |  |  | Code No .: |  |  |  |  | 

## Slide 17
Annexure-VI (Faulty BU Summary)
 |  |  |  |  |  | SUMMARY SHEET |  |  |  |  |  | Annexure-VI
STATE ELECTION COMMISSION - MADHYA PRADESH |  |  |  |  |  |  |  |  |  |  |  | 
Pre FLC ( DETAILS OF FAULTY BALLOT UNIT) |  |  |  |  |  |  |  |  |  |  |  | 
 |  | District : |  | Place of Testing : |  |  | Quantity : |  |  | Date : |  | 
Name of District => |  |  | District-1 | District-2 | District-3 | District-4 | District-5 | District-6 | District-7 | District-8 | District-9 | TOTAL
 |  |  | Count | Count | Count | Count | Count | Count | Count | Count | Count | COUNT
1 | Visual Inspection | Cabinet/ side lock broken |  |  |  |  |  |  |  |  |  | 
2 |  | Ballot Paper transparent screen broken |  |  |  |  |  |  |  |  |  | 
3 |  | Top cover side locks broken/ missing |  |  |  |  |  |  |  |  |  | 
4 |  | No of Candidates button masking tab broken/ missing |  |  |  |  |  |  |  |  |  | 
5 |  | No of Candidates button broken/ missing |  |  |  |  |  |  |  |  |  | 
6 |  | Connector hood broken |  |  |  |  |  |  |  |  |  | 
7 |  | Red latch of hood missing/ broken |  |  |  |  |  |  |  |  |  | 
8 |  | Black latch of hood missing/ broken |  |  |  |  |  |  |  |  |  | 
9 |  | Slide Switch broken |  |  |  |  |  |  |  |  |  | 
10 |  | Inerconnecting BU Cover broken |  |  |  |  |  |  |  |  |  | 
11 |  | Others (desribe few lines) |  |  |  |  |  |  |  |  |  | 
12 | Operational Inspection | Ready Lamp Not Glowing |  |  |  |  |  |  |  |  |  | 
13 |  | Ready Lamp glow continuous |  |  |  |  |  |  |  |  |  | 
14 |  | Candidates button LED glow continuous (No/s) |  |  |  |  |  |  |  |  |  | 
15 |  | Candidates button LED not glowing (No/s) |  |  |  |  |  |  |  |  |  | 
16 |  | Pressed Error |  |  |  |  |  |  |  |  |  | 
17 |  | Link Error |  |  |  |  |  |  |  |  |  | 
18 |  | 9 to 16 candidates lamps ON (BU Tampered) |  |  |  |  |  |  |  |  |  | 
19 |  | Slide Switch not working |  |  |  |  |  |  |  |  |  | 
20 |  | No of Buttons Not Working |  |  |  |  |  |  |  |  |  | 
21 |  | Connector/ cable problem |  |  |  |  |  |  |  |  |  | 
22 |  | Others (desribe few lines) |  |  |  |  |  |  |  |  |  | 
 |  |  | Tabulated By : |  |  |  |  |  |  |  |  | 
 |  |  | Signature : |  |  |  |  |  |  |  |  | 
 |  |  | Name .: |  |  |  |  |  |  |  |  | 
 |  |  | Code No .: |  |  |  |  |  |  |  |  | 

## Slide 18
Mock poll
Randomly pick up 1% of CUs & Three BUs for every one CU from the Pre FLC completed lot and carry out mock poll for at least 300 votes.
A batch of 10 or 20 EVMs can be set up at a time for this activity. After completion of the mock poll, verify EVM result with manually recorded votes. Then close the EVMs.

## Slide 19
Mock poll
The following test set up and candidate set configuration to be followed.
One CU with DMM and Three BUs
Number of Posts : 3 ( Three),
Post 1: candidates: 15, Seats: 14
Post 2: candidates: 15, Seats: 14
Post 3: candidates: 15, Seats: 14
Do mock poll and record the voting pattern for at least 300 votes.
Also perform few Under votes for each post and Unfinished voters choices and carefully keep the manual record of under votes & unfinished voters in the Form no. MP SEC EVM-FLC-01 (Annexure-VII) titled Manual Record for Under votes & Unfinished Voters.
Verify the Result with the manual mock poll records.

## Slide 20
Notes on Under votes
If voter chooses to press END button without voting for required number of seats that unselected seats are treated as under votes by the machine.
Example:
For above mentioned candidates if a particular voter voted in the following manner
Post 1 voted for 12candidate(s), Post 2 voted for selective10 candidates and Post 3 voted for selective eight candidates and Pressed END button.
Result:
Under votes for Post 1 = (Number of seats (14) – Actually polled votes (12)) = 2
Under votes for Post 2 = (Number of seats (14) – Actually polled votes (10)) = 4
Under votes for Post 3 = (Number of seats (14) – Actually polled votes (8)) = 6

## Slide 21
Notes on Unfinished Voters
If any voter chooses not to press END button(OR forgot) without voting for required number of seats, provided minimum one candidate must have selected.
This particular case machine needs to be restarted(Turn OFF and ON EVM) for further operation. That particular voter is treated as unfinished voter and the numbers of unselected seats are treated as under votes by the CU.
Example:
For above mentioned candidate set if a particular voter voted in the following manner.
Post 1 voted for 10 candidates, Post 2 voted for two candidates and Forgot to Press END button.

## Slide 22
Notes on Unfinished Voters Contd..
Note:
Now machine waits indefinitely for remaining unselected seats. Hence machine need to be restarted for further operation. After restart observe the following result for above voting pattern
Result:
Unfinished Voters = 1
Under votes for Post 1 = (Number of seats (14) – Actually polled votes (10)) = 4
Under votes for Post 2 = (Number of seats (14) – Actually polled votes (2)) = 12
Under votes for Post 3 = (Number of seats (14) – Actually polled votes (0)) =14

## Slide 23
Annexure-VII (Mock poll record)

## Slide 24
Requirements
Miscellaneous tools & stationary
Pre FLC Stickers (Annexure I & II)
Report Formats (Annexure III to VI)
Mock Poll Record Format (Annexure VII)

## Slide 25
Thank You